## Slide 1
Tree spotting
-mapping the urban tree canopy
Frank Hanssen
URBAN EEA Conference
Oslo March 18.th 2020
Photo: Inge Knoff (CC BY-NC 2.0)

## Slide 2
Photo: Frank Hanssen (CC BY-NC 2.0)
Outline
Context: The Oslo City Council aims to plant 100 000 new trees by 2030
How to account the achievement of this goal from using LIDAR-data?
What are the patterns of development from 2011 to 2017 in the built-up area of Oslo?
What are the application, limitations and uncertainity of our results?
Some reccomendations for future tree canopy mapping

## Slide 3
Data and
methodology

## Slide 4
Point category | Categories
1 | Unclassified
2 | Ground
3 | Low vegetation
4 | Medium vegetation
5 | High vegetation
7 | Outliers (noise)
9 | Water
10 | Points on bridge
13 | Wire-guard (shield)
24 | Power line
 | Average point density per m2 | Point classification
Oslo 2011 | 43 | 1-2-3-4-5-7-9-10-24
Oslo 2014 | 25 | 1-2-7-10
Oslo 2017 | 10 | 1-2-7-10-13
Data source: https://hoydedata.no/LaserInnsyn/

## Slide 5
Canopy Height Model (CHM)
CHM and vegetation mask
Estimation of tree canopy (1/2)

## Slide 6
Segmented tree canopies
Segmented tree canopies masked for technical infra-structure (buildings, powerlines, poles, signs, etc).
Estimation of tree canopy (2/2)

## Slide 7: Validation
At single tree level
  Underestimation in number of trees compared to PBE field data (70 % overlap)
  Local overestimation of tree canopy area compared to Sentinel 2
At aggregated level
  High correlation of tree canopy area compared to Sentinel 2 at city-district level
Hanssen et al. (2018). Mapping urban tree canopy cover using airborne laser scanning- applications to urban ecosystem accounting for Oslo. NINA-report 1677

## Slide 8
Results
Photo: Unknown (CC BY-SA)
So, how to account the achievement of the 2030 goal?
.. and what are the patterns of development (2011-2017)?

## Slide 9
2011
2014
2017
Crown
area
No. of
trees
Status in the built-up area compared to the 2030-goal
(2017 trees + 100 000 new trees = 100 %)

## Slide 10
Chart: Tree canopy area in the built-up zone per SSB land use category (ha)
| Agriculture | Commercial | Forestry | Freshwater | Green space | Industrial | Mire | Open landscape | Public service | Residential | Sea | Transportation | Unclassified
2011 | 37.2493 | 53.0037 | 1448.7857 | 26.1957 | 145.0679 | 53.7567 | 6.5292 | 174.1035 | 165.123 | 704.2973 | 0.69762 | 341.6023 | 258.8682
2014 | 39.9004 | 62.3868 | 1746.6317 | 30.7612 | 154.5103 | 61.7698 | 7.8492 | 191.4091 | 188.6077 | 770.6179 | 1.2974 | 433.2552 | 284.6574
2017 | 39.0621 | 63.0708 | 1796.3059 | 31.5758 | 158.0255 | 63.9291 | 7.57 | 208.0474 | 196.0577 | 782.1093 | 1.0075 | 407.5688 | 280.3074

## Slide 11
Number of trees in the «built-up» area
Number of tree in the «småhusplan» area of Oslo
Hanssen et al. (2018). Mapping urban tree canopy cover using airborne
laser scanning- applications to urban ecosystem accounting for Oslo.
Median height 2011: 14
Median height 2014: 11
Median height 2011: 11
Median height 2011: 15
Median height 2014: 15
Median height 2011: 16

## Slide 12
Chart: Change in tree crown area (ha)
| 2011 | 2014 | 2017
Småhusplan area trees 2.5 - 11 m | 184.4981 | 275.1198 | 285.2368
Småhusplan area trees 12 - 35 m | 635.8266 | 611.9859 | 571.7747
Småhusbebyggelse area trees 2.5 - 11 m | 394.3246 | 554.1121 | 538.7095
Småhusbebyggelse area trees 12 - 35 m | 1464.624 | 1557.4571 | 1484.5722

## Slide 13
Change in tall trees in the
«Småhusplan area»
Change in tall trees in the
«Småhusbebyggelse area»

## Slide 14
Nordre Aker
Notes: Dette kan være en indikasjon på at reguleringene i småhusplanområdet på å felle store trær har en effekt.

## Slide 15
Application, limitations and uncertainity
City level
- Green citywide accounts
City sub-district level
- Green accounts. Neigbourhood level access to greenviews per capita
Public parks & street level
- Inventory of managed trees’ canopy
surface and volume for ecosystem
service estimation
Property level
- Calculating number of trees and
canopy cover for blue-green factor
- Prediction of shading and insolation
Single tree level
- Monitoring large trees (“Småhusplan”)
High
confidence
Low
confidence

## Slide 16
Foto: Frank Hanssen (CC BY-SA 4.0)
Reccomen-dations
Future LIDAR campaigns should be designed for vege-tation mapping, and combined with IR og hyper-spectral imagery.
We reccomend to migrate future segmentation to cloud computing platforms (e.g. Google Engine) due to its computation capacity.
More field data is needed for the validation of tree canopy data based on remote sensing data.
Segmentation methods needs to be refined for
tree canopy mapping within an urban environment

## Slide 17: Thank you for your attention!
Questions?
frank.hanssen@nina.no